## Slide 1
EXECUTIVE SUMMARY
Prepared for :
Techno Economic Feasibility Report : Epoxy Resin
MARKET INTELLIGENCE | CONSULTING
www.techsciresearch.com

## Slide 2
Properties, Application & End Use
Epoxy resins are thermosetting polymer, which crosslink & polymerize when mixed with the catalytic agent or “Hardener”. Epoxy resin is usually synthesized by bulk polymerization. The material is available commercially at 98% purity & are colourless. Many commercial liquid resins consist essentially of low molecular weight diglycidyl ether of Bisphenol A together with small quantity of higher molecular weight polymer. In general, production of bisphenol A epoxy resin is divided into one step method & two-step process method. In one-step method, Bisphenol A reacts directly with epichlorohydrin in order to prepare epoxy resin, which commonly used for the synthesis of low to medium molecular weight (MW) epoxy resins.
Grades | Properties | Applications
Bisphenol A Liquid Epoxy Resin | Viscosity range - 450 to 26000 mPa-s | Paints and Coatings (Coating Ingredients/ Ink Ingredients), Construction
Bisphenol A Solid Epoxy Resin | Viscosity range between 160 to 10,000 mPa.s | Paints and Coatings (Coating Ingredients/ Ink Ingredients), Construction (Floor Coating Materials/ Linings/ Civil Engineering
Bisphenol F Liquid Epoxy Resin | low viscosity low crystallization tendency | Paints and Coatings (Adhesives/ Adhesive Ingredients, Electrical and Electronics (Impregnation/ Lamination/ FRP Molding)
Brominated (Flame Retardant Types) Epoxy Resin | High bromine type, solid content 60% toluene solution | Electrical and Electronics (Impregnation/ Lamination/ FRP Molding),
Cresol Novolac Epoxy Resin | High viscosity | Electrical and Electronics (Impregnation/ Lamination/ FRP Molding), Adhesives/ Adhesive Ingredients
 | High epoxy index | 
Phenol/Modified Novolac Epoxy Resin | Viscosity at 52°C (126°F): 600-50,000 cP. Epoxide equivalent weight (EEW): 160 – 270 g/eq. | Electrical and Electronics (Impregnation/ Lamination/ FRP Molding), Adhesives/ Adhesive Ingredients, Composites
Cycloaliphatic Epoxy Resin | . Viscosity at 25 degree C Cp - 1800-2500 | Electrical and Electronics (Impregnation/ Lamination/ FRP Molding),
Dimer Acid modified epoxy resin | Viscosity -50000 cps@52 degree Celsius, EEW (g/eq) – 660 | Adhesives/ Adhesive Ingredients
Mass Balance |  |  | 
Input | T/T | Output | T/T
Bisphenol A | 0.74 | Product | 1
Epichlorohydrin | 0.56 | Solid Waste | 0.096
48% NaOH | 0.50 | Reaction Water | 0.33
Total | 1.76 | Total | 1.76
Waste Disposal : While industrial production of Epoxy Resins, by-products like NaCl and oligomers are also released. NaCl can be removed by washing with water one or more times, depending on the reaction requirement. An aqueous solution of sodium chloride called Brine formed resultantly can be further send to ETP plant for its treatment to decrease its concentration to the optimum level so that it can be disposed to sea or can be sent to Pollution control Board for further use. The resin is separated through filtration while solid polymeric particles (with high K-value) are discarded in a manageable way such as through landfilling. Manufacturers must essentially maintain an adequate ratio of ECH and BPA while Epoxy Resin manufacturing to minimize the waste generated.

## Slide 3
Demand-Supply Scenario : Global, Europe and Domestic
(000 Tonnes) | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2025 | 2030 | 2035 | CAGR (2010-2021) | CAGR (2021-2035)
Global Supply | 2545.8 | 2387.7 | 2480.0 | 2596.8 | 2751.5 | 2866.3 | 2986.4 | 3150.6 | 3328.4 | 3470.4 | 3246.2 | 3494.4 | 3724.0 | 4119.0 | 4150.0 |  | 
Global Demand | 2348.3 | 2194.2 | 2352.1 | 2484.5 | 2611.1 | 2753.9 | 2891.3 | 3110.4 | 3187.1 | 3364.6 | 3261.1 | 3493.9 | 4399.7 | 5511.3 | 6746.7 | 3.7% | 4.8%
Gap |  |  |  |  |  |  |  |  |  |  |  |  | -675.7 | -1392.3 | -2596.7 |  | 
Europe Supply | 491.9 | 480.8 | 498.2 | 490.2 | 505.2 | 525.5 | 541.8 | 562.9 | 670.0 | 695.9 | 621.1 | 676.8 | 741.0 | 812.2 | 820.5 |  | 
Europe Demand | 455.7 | 428.7 | 442.5 | 465.3 | 483.7 | 506.8 | 530.3 | 554.7 | 573.7 | 599.4 | 550.6 | 582.0 | 675.1 | 821.8 | 970.4 | 2.2% | 3.7%
Gap |  |  |  |  |  |  |  |  |  |  |  |  | 66.0 | -9.6 | -150.0 |  | 
 | FY 2011 | FY 2012 | FY 2013 | FY 2014 | FY 2015 | FY 2016 | FY 2017 | FY 2018 | FY 2019 | FY 2020 | FY 2021 | FY 2022 | FY2026 | FY2031 | FY2036 |  | 
India Supply | 35.2 | 37.7 | 40.1 | 42.7 | 46.8 | 55.7 | 68.6 | 89.1 | 89.7 | 101.6 | 93.9 | 112.1 | 193.5 | 206.3 | 210.0 |  | 
India Demand | 44.2 | 47.9 | 51.3 | 55.3 | 58.8 | 65.4 | 71.8 | 79.7 | 89.5 | 103.0 | 88.7 | 98.3 | 141.7 | 201.0 | 295.6 | 7.5% | 8.2%
Gap |  |  |  |  |  |  |  |  |  |  |  |  | 51.8 | 5.3 | -85.6 |  | 
Basis for Demand-Supply Gap
The basis of the historic data is secondary databases like annual reports of the competitors, import-export and other socio-economic factors. Forecast has been done through forecast model and primary responses of key opinion leaders. Forecasting generally assumes overall economic stability and no significant changes in the industry or market.
Historical conditions in the past will not carry over into the future.
Operating rate for new unit is considered as 60 percent for 1st year and 90 percent later.
Crude oil and commodity prices are likely to stabilize from 2nd half of 2022 onwards.
Covid-19 situation is likely to dimmish from 2023 onwards after global roll out of vaccination.
Increased investment in infrastructure and construction sector.
BRIC nations will have higher growth in comparison to North America and Europe
Increased expenditure in research and development will lead to increased usage of superior grades.
Demand of Liquid and Solid Epoxy Resin witnessed a strong demand from Auto and Consumer durable leading to uptick in realization and sales volume in China, India, South Korea and Thailand.
Construction industry will be focusing on major investments in the housing, energy, and utility infrastructure.
Growing IoT ecosystem is expected to uplift demand for electronics products in coming years. Northeast Asia, with the highest concentration of electronic component manufacturing, seems to be making aggressive moves towards expanding their facilities
Demand for composites from renewables, marine and aerospace are rising due to rapid urbanization and industrial and aviation sector growth and considerable opportunities exist for specialized epoxy resin manufacturers.
Coating
Construction
Electronics
Composites

## Slide 4
Suggested Capacities
Source: TechSci Research
Suggested Capacity in Tonne |  | FY2025 | FY2030
Upstream | LER | 22,000 | 44,000
Downstream |  |  | 
 | Solid | 10,000 | 20,000
 | Semi Solid | 3,000 | 6,000
 | Specialized | 7,000 | 14,000
Total Capacity |  | 42,000 | 84,000
Operating Rate |  | 60.00% | 95.00%
Production (By Grade) | LER | 13,200 | 41,800
 | Solid | 6,000 | 19,000
 | Semi Solid | 1,800 | 5,700
 | Specialized | 4,200 | 13,300
Total Production |  | 25,200 | 79,800
Demand-Supply Gap (Optimistic) (India) |  | 51,500 | -34,600
TechSci Research suggested 84, 000 Tonnes of epoxy resin capacity to be executed in two phases, Capacity Build Up – 1st Year: 60 %, 2nd Year : 80 % and 3rd Year : 95% By FY 2029 onwards, RIL can easily capture significant market share of incremental demand due to widening demand supply gap. Initially, RIL needs to export most of the production as India is likely to be surplus for LER, SER and SSER. The capacity recommendations is based on the assumption that all these target end use sectors will attract heavy investments towards planned milestones supported by the positive government regulatory and investment environment by FY2030.
Production Meant Sale (In Tonnes) | India | FY2025 | FY2030
Upstream | Liquid Epoxy Resin | 13,200 | 41,800
 | Captive | 5,800 | 18300
 | Domestic Merchant Sale | 1,500 | 23400
 | Export | 5,900 | 0
Downstream | Solid | 6,000 | 19,000
 | Captive | 0 | 0
 | Domestic | 2,000 | 12,000
 | Export | 4,000 | 7,000
 | Semi-Solid | 1,800 | 5,700
 | Captive | 0 | 0
 | Domestic | 400 | 3,500
 | Export | 1,400 | 2,200
 | Specialized | 4,200 | 13,300
 | Captive | 1,500 | 4,500
 | Domestic | 400 | 3,500
 | Export | 2,300 | 5,300
• Significant demand-supply gap in local and overseas markets during the forecast period : Evaluation of both Indian and international epoxy resin markets reveal a significant demand-supply gap in the period of forecast. Epoxy Resin demand is likely to outpace the supply due to strong demand growth in the downstream construction and automotive sector. Demand in India for advanced Epoxy-based materials is expected to remain strong with growing thrust on renewables, and thin inventory across product segments.
• Suggested capacity volume considering optimistic scenario of the market and anticipations of contracts with various end-user industries : The Indian epoxy resin industry is strongly reacting towards certain plant shutdowns / lower operating rate due to rising environmental concerns in China and global trade shift with several players are eyeing on grabbing the market share amidst the latest demand-supply mismatch. In addition, Indian players are expecting long-term sales and price contracts with bulk manufacturers in the downstream markets placed both in domestically and internationally in the coming years. Higher capacity than the calculated gap is considering the healthy consumption trend with country’s growing focus over strengthening its domestic manufacturing.
RIL being a major in commodity polymers and fibre intermediates will likely benefit from its global brand positioning to utilise the access Epoxy Resin capacity. RIL could ramp up exports by up to 30% during initial year of operation of its new capacity

## Slide 5
Competing and Possible Disruptive Material
Bio Based Epoxides
Bio Based Epoxides
Bio based epoxy resins are bio sourced resins which are produced by the epoxidation of renewable feedstocks such as unsaturated vegetable oils, saccharides, lignin, tannins, cardanols, terpenes, rosins etc. The resins are cured with the help of co-reactants called hardeners. The type of hardener depends upon the type of epoxy resin. The hardener itself can also be biobased.
Some of the biobased epoxy resins available in the market are Greenpoxy, Entropy Resins, Sicomin Epoxy Systems, One Epoxy, Wessex Resins, etc.
Sucrose Based Epoxides :
Chemical Looping
Chemical-looping combustion (CLC) and chemical-looping reforming (CLR) are two processes that are potentially cost-effective carbon dioxide capture options with minimum energy losses, in which both CO2 and H2O are inherently separated from flue gas. For pre-combustion CO2 capture, chemical looping can be combined with IGCC to produce syngas as a valuable by-product. These technologies use a metal oxide as an oxygen carrier to circulate oxygen between the air and fuel reactors; thus, their large-scale applications are highly dependent upon the availability of suitable oxygen carriers.
Epoxy resin inorganic nanocomposite
Circularity for thermoset epoxy composites : The new technology delivers the final technological step on the journey towards a fully recyclable wind turbine value chain.

## Slide 6
Business Model
Domestic Players and Their Business Model
Global Players and Their Business Model
Company | Technology | Process | FY2022 | FY 2025
Grasim Industries Ltd. | Tohto Kesia | BADGE & Advancement | 66 | 90
Atul Limited | Ciba-Geigy | BADGE & Advancement | 40 | 50
Kukdo Chemical India Private Limited | In house Technology | Advancement | 40 | 40
Hindusthan Specialty Chemicals Ltd | JEIL Chemical Ltd. & Wuxi Bluestar | BADGE & Advancement | 30 | 30
Meghmani Finechem Limited | In house Technology (Solv | BADGE & Advancement | 0 | 25
Total |  |  | 176 | 235
Company Name | Business Model
Atul Ltd. | Diverse product Portfolio, help the company in tapping domestic and export market. For Instance, Bisphenol F, GL accredited epoxy systems for wind blade manufacturing, etc.
Grasim Industries Ltd. | Strong Brand Image, Networking and Supply Chain Management.
Hindusthan Specialty Chemicals Ltd | Highly competitive and Strong Business Strategies pushing the company in gaining domestic market share.
Kukdo Chemical India Private Limited | Strong Backup from parent company, availability of raw material at below par from parent organization help me building brand in domestic market.
Company Name | Business Model
Olin Corporation | Extensive Supply Chain coupled with strategic location help in strong hold of company across the globe.
Nan Ya Plastics Corporation | Strong hold in Asia Pacific region and one of the largest exporter of Epoxy resin.
Kukdo Chemical Co., Ltd. | Strong R & D and Diversified product portfolio, help in gaining market share.
Huntsman Corporation | Strong hold in Europe and USA market coupled with growing export potential from USA.
Hexion Inc. | Strong Presence in North America and Europe with strong demand from Europe is the deriving factor.

## Slide 7
Business Environment
Cost competitiveness against Domestic / South Korean* / European Manufacturer**
Few Players in domestic market.
Low Entry barrier for epoxy market.
Strong brand image and leading market player in domestic and international market.
Strong distribution network.
Diversified Product portfolio and currently serving paints & coatings industry.
Strong growth in Paint & Coating Industry.
Strong network and better optimization of resources.
RIL can produce Epoxy resin using Bisphenol-A, which can be further treated to produce polycarbonate and other derivatives products.
RIL is currently one of the major exporter of Petrochemicals products from India. RIL having strong market hold in domestic and export market, which will help the company in gaining market shares.
Sourcing of raw material and long term contract price of raw material will help RIL in lower operational cost.
RIL is having an upper edge as the company can produce products by forward integration such as polycarbonates etc which other domestic players are lagging.
Globally known brand which will help RIL in tapping the export market especially Europe and Asia Pacific region.
Competitive advantage against Domestic / South Korean* / European Manufacturer**
Competition & Key Success factors.

## Slide 8
India, Europe and Asia Pacific Export Potential 2010-2020, 2025F, 2030F, 2035F ( Thousand Tonnes)
 | 2010 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2025F | 2030F | 2035F
India Export | 8.2 | 20.2 | 26.4 | 29.1 | 30.8 | 29.9 | 19.7 | 24.8 | 34.3 | 49.6
India Import | 38.9 | 51.4 | 57.8 | 59.3 | 47.1 | 55.1 | 44.2 | 57.2 | 69.2 | 45.3
Europe Import | 510.8 | 573.2 | 591.5 | 604.1 | 585.6 | 557.4 | 506.8 | 636.7 | 879.9 | 1273.2
Asia Pacific Export | 685.2 | 751.7 | 779.3 | 855.6 | 816.1 | 833.1 | 855.3 | 1106.3 | 1339.7 | 1567.8

## Slide 9
Economic Analysis
Licensed Capacity 84 KTPA
Total Investment
USD Million 35.77
NPV
USD Million 140.95
IRR
54.66%
Payback (Yrs.)
2.34
Chart: 
| Operating Revenue | Working Capital Change | Gross Profit | Total Operating Cost | Gross Margin | Net Cash Flow
Series 1 | 89.21 | 8.47 | 97.65 | 75.49 | 13.72 | 12.11
Chart: Annual Cost Of Production-Liquid Epoxy Resin
| Total Fixed Cost | Total Variable Cost
Sales | 0.0117 | 0.9883
Chart: Operational Expenditure in FY 2024 (In USD Million)
| Total Production Cost | Selling Overheads | Fixed Overheads | Variable Overheads | Labour | Raw Materials
Series 1 | 256.78 | 25.64 | 2.79 | 11.71 | 2.56 | 214.08
Chart: Capital Expenditure (USD Million)
| Total Direct Plant Cost | Total Indirect Plant Cost | Working Capital | Total Capital Investment
Series 1 | 25.32 | 9.68 | 0.77 | 35.77
Project Sensitivity Analysis | 
Break Even Point at Optimum Capacity Utilization (3rd Year) | Particulars
Revenue in 3rd Year (USD Million) | 137.77
Expenses in 4th Year (USD Millio) | 113.62
Break Even Point | 54.66%
Project Sensitivity* | 
Present Break even Point | 54.66%
Revenue remains same, Expenses increase by 5% | 86.59%
Revenue decreases by 20%, Expenses remain same | 103.09%
Revenue decreases by 20%, Expenses increases by 10% | 113.40%
Revenue decreases by 20%, Expenses increases by 20% | 123.71%
Revenue decreases by 10%, Expenses increases by 10% | 100.80%

## Slide 10
Technology Overveiw
Technology | Open for Third Party Licensing
Ciba-Geigy AG | 
Tohto Kasei Co. Ltd. | 
Kukdo Chemical Co., Ltd | 
Olin Corporation | 
Dow Chemicals | 
JEIL | 
Wuxi Bluestar | 
Only two of the following licensors i.e., Ciba-Geigy AG and Tohto Kasei Co., Ltd are open to share the technologies with new entrants.
Both the technologies give favorable outcomes qualitatively & quantitatively. Also, both technologies are being used in India by leading epoxy resin manufacturers like Grasim Industries and Atul Ltd.
Kukdo Chemical Co., Ltd and Olin Corporation do not share the technological process and process parameters and employ the manufacturing process in its own specific plants.
The quality of product provided by Kukdo Chemical Co., Ltd is very superior in comparison to other technology licensors and it provides crystal clear liquid epoxy resin to the clients.
Ciba- Geigy AG has low solvent requirements than the Tohto Kasai Co., Ltd.
Re-engineering Epoxy’s Hardening Component-
Recylamines are prepared by mixing bisphenol A diglycidyl ether with curing agents having amine groups that react with the ether’s epoxide groups to result into hard cross-linked molecules. Recyclamine is the only type of completely recyclable epoxy resin adopted in India till date. Aditya Birla Chemicals acquired the use of Recyclamine Technology from Connora Technologies in 2019. The great thing about epoxies with Recyclamine hardeners is that they can be completely recycled without pyrolysis.
Sicomin and biobased epoxy resins-
Bio based epoxy resins are bio sourced resins which are produced by the epoxidation of renewable feedstocks such as unsaturated vegetable oils, saccharides, lignin, tannins, cardanols, terpenes, rosins etc. Sicomin is a leading manufacturer and formulator of advanced epoxy systems. The company manufacturers epoxy systems for application in aerospace, defence, marine, renewable energy, sports, and civil engineering. Some of the biobased epoxy resins available in the market are Greenpoxy, Entropy Resins, Sicomin Epoxy Systems, One Epoxy, Wessex Resins, etc.
Direct Emissions- There is no GHG emissions reported during the production process of epoxy resin. As per industry experts, ECH emissions has been observed during the production process.
Indirect Emissions- During the incineration process, CO2 and CO is released which are within the permissible limit. As per industries experts, these emissions can be prevented by the installation of different wet scrubbers.