## Slide 1
MARKET INTELLIGENCE . CONSULTING
www.techciresearch.com
TECHNO-ECONOMIC FEASIBILITY REPORT
FOR VINYL ESTER RESIN MANUFACTURING
Prepared for:
© TechSci Research

## Slide 2
Final Findings
Product Name | Demand Supply Gap -2025 | Demand Supply Gap -2030 | Export Potential | Backward Integration | Forward Integration | Recommendations
Unsaturated Polyester Resin | Medium | High | Yes | Yes | No | Project can be planned by 2023
Vinyl Ester Resin (BPA) | Medium | High | Yes | No | Yes | Project can be planned by 2023
Vinyl Ester Resin (BPF) | Low | Medium | Yes | No | Yes | Project can be planned by 2023
Vinyl Ester Resin Novolac | Medium | High | Yes | No | Yes | Project can be planned by 2023

## Slide 3
Recommendations for setting up facilities for production of Vinyl Ester Resin considering the returns of investments and economic of scale
Name of the Product (KTPA) | 2023 | 2027 | Total
Unsaturated Polyester Resin | 25 | 25 | 50
Vinyl Ester Resin | 15 | 15 | 30
RIL may consider setting-up a 30 thousand tonnes vinyl ester resin unit as enough scope exists from demand – supply point of view.
Considering the return of investment and economic viability of the project, the Reliance Industries Ltd. should plan the project in two phases i.e., in 2023, they can plan for 25 KTPA and 15 KTPA capacity for Unsaturated Polyester Resin (UPR) and Vinyl Ester Resin (VER), respectively and in 2027, according to the demand scenario, they can expand the capacity by 25 KTPA and 15 KTPA for UPR and VER, respectively.
Globally, Reliance Industries Ltd. is among the top 10 producers for key petrochemicals. Reliance Industries Ltd. has incorporated a separate business unit for their oil to chemical business as Saudi Aramco holds a possible stake due to which this project has global importance and viability.
Reliance Industries Ltd. being the globally renowned company, is expected to produce high quality products with the latest technology to compete with global players. For export market, the company needs to compete and match the quality of the existing global players such as AOC Resins, INEOS Composites, Showa Denko etc. With no technology licensor for vinyl ester resin, the company needs to produce superior quality product or can either collaborate with the existing global players to match the international quality of the product.
Reliance Industries Ltd. should focus on Bisphenol –A and Novolac based vinyl ester resin due to their extensive use in major end user industries like pipes and tanks, renewables, marine components, electronic & electricals, defense, automotive etc.

## Slide 4
With growing demand for Vinyl Ester Resin in various sector such as wind energy, transportation, electrical and electronics, defense, aerospace, pipes and tanks, construction and marine, companies have started investing in expanding manufacturing facilities for the production of VER. For instance, Showa Denko has expanded its manufacturing facility in Japan.
With the emerging application of vinyl ester resin i.e., in electronics and telecommunication, due to its use in the process to produce electronic parts including LCDs and touch panels, which has been rapidly increasing in APAC region mainly in China is anticipated to boost the demand of VER for the forecast period.
The future wave in the telecom industry is the 5G network, which covers less distance than the existing 4G network. In India, the Ministry of Telecommunications and The Telecom Regulatory Authority of India (TRAI) plans to implement 5G in the coming years. With this implementation, usage of VER for the telecom industry is expected to register strong growth in the coming years.
The increasing use of vinyl ester resin in automotive sector where it is used for molding structural parts, especially automotive components to reduce weight like in the seats, wheels, cooling rack, the engine valve sleeve and other automotive parts are applied.
Demand Drivers – Vinyl Ester Resin
Expected Growth – Vinyl Ester Resin
  Government support in India to increase per capita consumption of FRP composites
  Growing usage as Lining System in Industrial Applications
  Robust Growth of Construction Sector
  Aging Infrastructure
  Rising Investment in Renewable Energy
  Reducing global carbon dioxide (CO2) emissions to net zero by 2050
  Stable macroeconomic factors, Stable lending rate
  Potential export market due to China factor (movement of manufacturing to India)
Expected Growth & Key Market Drivers

## Slide 5
Challenges During The Forecast Period
1
  Some of the raw materials used in the manufacturing of vinyl ester resin is 100% import driven like styrene, therefore handling may be the challenge.
2
  Cost Escalation- As commodity prices like steel, natural gas, coal & electricity are increasing therefore machinery & equipment cost may increase in the forecast period.
3
Currency fluctuations also plays a major challenge in the manufacturing of vinyl ester resin as most of the raw materials are hundred percent import driven.
4
Recessionary factors like wholesale inflation, GDP contraction, fiscal deficit may be the challenging factors which can impact the demand supply scenario of vinyl ester resin.
As the demand of vinyl ester resin is entirely project based therefore demand fluctuation may be the major threat to the market of vinyl ester resin.
5
Research and Development cost may increase as Reliance needs to compete with global players for niche and specialized applications. Moreover, for export of vinyl ester, Reliance should focus on international quality specification of VER.
6
High Volatility in Raw Material Prices.
7
Fragmented Market of Composites industry in China and India.
8
With the increase in global prices of crude oil, natural gas, coal & electricity, the rise in consumer price inflation(CPI) have been seen which may impact the market of vinyl ester resin.
9

## Slide 6
Observation on project cost, viability and sensitivity on fluctuation in feedstock and product prices
Project is moderately sensitive to variations in investment and highly sensitive to selling Price and feedstock prices. The project is not capital intensive and can be easily funded through internal accruals. Equipment require for the project are available in domestic and international market and can be easily sourced. The technology, catalyst and chemicals are also easily available.
Several downstream consumers of Epoxy Resins including VER reported pressured margins due to unexpected surges in Epoxy Resin and styrene pricing in 2021. It is estimated that the market price of key raw materials will remain at high levels in next few years, with slight fluctuations. Most of the producers are not in position to pass on the increase raw materials to end-users.
NPV in USD Million |  |  |  |  | 
 | BASE CASE | 90.00% | 95.00% | 105.00% | 110.00%
 | REVENUE |  |  |  | 
IRR% | 50.02% | 27.48% | 39.23% | 60.22% | 70.04%
NPV | 31.4 | 10.6 | 21 | 41.8 | 52.2
 | RAW MATERIALS COST |  |  |  | 
IRR% | 50.02% | 63.99% | 57.09% | 42.71% | 35.09%
NPV | 31.4 | 45.8 | 38.6 | 24.2 | 17.1

## Slide 7
Representative list of clients

## Slide 8
About Us & Disclaimer
TechSci Research is a global market research and consulting company with offices in the US, UK and India. TechSci Research provides market research reports in number of areas to organizations. The company uses innovative business models that focus on improving productivity, while ensuring creation of high-quality reports. The proprietary forecasting models use various analyses of both industry-specific and macroeconomic variables on a state-by-state basis to produce a unique ‘bottom-up’ model of a country, regional and global industry prospects. Combined with the detailed analysis of company activity and industry trends, the result is a uniquely rich evaluation of the opportunities available in the market.
Related Reports
Global HBPA Epoxy Resin Market By Physical Form (Solid and Liquid), By Application (Industrial Coating, E&E Coating and Others), Competition, Forecast & Opportunities, 2026
Global Composites Market By Type (Glass Fiber & Carbon Fiber), By Application (Civil Engineering, Aerospace & Défense, & Others), By Manufacturing Process (Lay Up, Injection Moulding, etc.), By Region, Competition Forecast & Opportunities, 2012-2026
The contents of this report are based on information generally available to the public from sources believed to be reliable. No representation is made that it is timely, accurate or complete. TechSci Research has taken due care and caution in compilation of data as this has been obtained from various sources including which it considers reliable and first hand. However, TechSci Research does not guarantee the accuracy, adequacy or completeness of any information and it is not responsible for any errors or omissions or for the results obtained from the use of such information and especially states that it has no financial liability whatsoever to the subscribers / users of this report. The information herein, together with all estimates and forecasts, can change without notice. All the figures provided in this document are indicative of relative market size and are strictly for client’s internal consumption. Usage of the same for purpose other than internal will require prior approval of TechSci Research.
TechSci Research – North America
708 Third Avenue, Manhattan,
New York, United States
Tel: +1- 646- 360- 1656
Email: sales@techsciresearch.com www.techsciresearch.com
Disclaimer
TechSci Research – Europe
54, Old brook, Bretton,
Peterborough,
United Kingdom
Email: sales@techsciresearch.com www.techsciresearch.com
TechSci Research – Asia-Pacific
B – 44, Sector – 57, Noida, National Capital Region, U.P. - India
Tel: +91-120-4523900
Email: sales@techsciresearch.com www.techsciresearch.com