## Slide 1
Executive Summary
Pre-Feasibility Report
PVC & Phenol: India
MARKET INTELLIGENCE . CONSULTING
www.techscireserach.com
October 27, 2022
Prepared For
Prepared By

## Slide 2
Contents
PVC
Phenol
PVC + Phenol
Annexure
04
24
46
50

## Slide 3
PVC

## Slide 4
India: Manufacturing Landscape
Source: TechSci Research
Hazira: RIL
Vadodara: RIL
Dahej: RIL
Dahej: RIL (Planned)
Dahej: OPaL (Upcoming)
4. Mundra: Adani (Planned)
5. Ratnagiri: Finolex
6. Kota: DCM Shriram
West
Paradip: IOCL (Planned)
East
Cuddalore: Chemplast
Cuddalore: Chemplast (Planned)
2. Mettur, Chemplast
3. Tuticorin, DCW Ltd.
South
India Polyvinyl Chloride (PVC) Capacity, By Company (000’ Tonnes)
Company | Technology Provider | Capacity, FY2021
Reliance Industries Limited | BF Goodrich, USA (now known as Oxy Vinyl) | 755
Finolex Industries Limited | Uhde, Germany | 272
Chemplast Sanmar Limited | BF Goodrich, USA (now known as Oxy Vinyl) | 366
DCW Limited | Atochem, France | 90
DCM Shriram Limited | Kureha technology | 70
1
2
3
4
6
5
1
1
2
3
All manufacturers offer suspension grade.
Finolex Industries Limited & Chemplast Sanmar Limited also offer emulsion grade.
PVC

## Slide 5
India: Capacity, Production
Source: TechSci Research
India Polyvinyl Chloride (PVC) Capacity and Production, By Volume (000’ Tonnes), 2010 - 2040F
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2035F | 2040F
Capacity | 1327 | 1501 | 1553 | 1553 | 1553 | 1807 | 4157 | 4157 | 4157
Production | 1191 | 1354 | 1475 | 1376 | 1388 | 1580 | 3350 | 4050 | 4050
Upcoming PVC Plant details
Company Name | Expected Capacity | Type of Process | Status
Indian Oil Corporation Limited | 500KTPA | EDC / VCM to PVC | Availability of chlorine is a major challenge (Location Disadvantage)
Adani Enterprises Limited | 1000KTPA | Coal to PVC | Submitted proposal for environmental clearance in April 2021.
Chemplast Sanmar Limited | 236 KTPA (Brownfield Expansion) for Suspension Grade PVC | VCM to PVC | Received the environmental clearance and the project is in initial phase.
Reliance Industries Limited | 1000 KTPA of Brownfield Expansion to produce S-PVC, Emulsion grade and C-PVC | Ethylene to PVC | Received the environmental clearance and. the project is in initial phase, expected to be commissioned by FY 2026.
ONGC Petro additions Limited | 350 KTPA Greenfield Expansion | Ethylene to PVC | The project is in Initial stage and is expected to be commissioned by FY 2027.
Upcoming Greenfield / Brownfield Projects will intensify the competition.
PVC

## Slide 6
Growing construction and agriculture sector is pushing the demand of PVC in India.
Government’s focus on Infrastructure development and low per capita consumption @ 2.24 kg, to drive future growth of the product.
India will become world’s third largest construction market by 2030, adding 12.7 million homes a year to become a USD1 trillion market
uPVC Windows market is growing at a CAGR of 10% because of growing acceptance by Indian Builders and Architects boosting. There is effort to introduce IS standard
Better market capitalization and lucrative demand of PVC in pipes and fittings.
AatmaNirbhar Bharat” and “Make in India” policies are pushing domestic manufacturer to produce green field capacity to promote domestic manufacturing in the country.
India: Demand
India Polyvinyl Chloride (PVC) Demand, By Volume (000’ Tonnes), 2010-2040F
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2040F
By Volume (Thousand Tonnes) | 1829.7825 | 2622.0085 | 3500.6472 | 2870.1545 | 3121.0169 | 3790.95 | 5350.86 | 10801.51
CAGR 2010-2021 | CAGR 2022E-2030F | CAGR 2031F-2040F
4.18% | 6.97% | 7.27%
Source: TechSci Research
India Polyvinyl Chloride Demand Supply Gap, 2010-2040F (000’ Tonnes)
Parameters | 2010 | 2015 | 2021 | 2022E | 2025F | 2030F | 2040F
Capacity | 1327 | 1501 | 1553 | 1553 | 1807 | 4157 | 4157
Production | 1191 | 1354 | 1376 | 1388 | 1580 | 4050 | 4050
Import | 659 | 1293 | 1595 | 1786 | - | - | -
Export | 0 | 2 | 75 | 27 | - | - | -
Inventory | 20 | 23 | 25 | 26 | - | - | -
Demand | 1830 | 2622 | 2870 | 3121 | 3791 | 5351 | 10802
Demand (Y-O-Y Growth Rate, %) | - | 15.63% | -18.01% | 8.74% | 6.85% | 7.31% | 7.00%
Demand - Supply Gap | - | - |  | (1733) | (2211) | (1301) | (6752)
PVC
Demand-Supply Gap arguments the need for new player, even post-realization of ongoing/upcoming Greenfield/Brownfield Projects

## Slide 7
India: Demand—Grade, End-Use,Type
India PVC Demand by Rigid & Flexible Type
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2040F
Flexible PVC | 0.1488 | 0.1421 | 0.1363 | 0.1533 | 0.153 | 0.1515 | 0.1485 | 0.1541
Rigid PVC | 0.8512 | 0.8579 | 0.8637 | 0.8467 | 0.847 | 0.8485 | 0.8515 | 0.8459
Total | 1,830 | 2,622 | 3,501 | 2,870 | 3,121 | 3,791 | 5,351 | 10,802
Source: TechSci Research
India Polyvinyl Chloride (PVC) Demand, By Type, By Volume, 2010–2040F (000’ Tonnes)
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2040F
Emulsion Polymerization | 0.0315 | 0.0491 | 0.0434 | 0.047 | 0.0464 | 0.0451 | 0.042 | 0.0425
Suspension Polymerization | 0.9685 | 0.9509 | 0.9566 | 0.953 | 0.9536 | 0.9549 | 0.958 | 0.9575
Total | 1,830 | 2,622 | 3,501 | 2,870 | 3,121 | 3,791 | 5,351 | 10,802
Used in manufacturing pipes and conduits.
India Polyvinyl Chloride (PVC) Demand, By End Use, By Volume (000’ Tonnes), 2010–2040F
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2040F
Others | 0.1361 | 0.0991 | 0.07 | 0.0968 | 0.094 | 0.0872 | 0.078 | 0.0783
Footwear | 0.0052 | 0.0057 | 0.0062 | 0.006 | 0.0065 | 0.008 | 0.0074 | 0.0051
Profiles | 0.0323 | 0.0334 | 0.0298 | 0.028 | 0.0283 | 0.0293 | 0.0306 | 0.033
Calendering (Films & Sheets) | 0.0606 | 0.0625 | 0.0607 | 0.0558 | 0.0563 | 0.0573 | 0.0594 | 0.0622
Wires & Cables | 0.0646 | 0.0675 | 0.081 | 0.0795 | 0.0805 | 0.0822 | 0.0854 | 0.0914
Pipes & Fittings | 0.7012 | 0.7318 | 0.7523 | 0.7339 | 0.7344 | 0.736 | 0.7392 | 0.73
Others include Medical & Healthcare, Vinyl Flooring, etc.
Total | 1,830 | 2,622 | 3,501 | 2,870 | 3,121 | 3,791 | 5,351 | 10,802
Suspension Grade is the most prominent type
Pipes & Fittings is the most prominent end-use
Rigid PVC is the most prominent type
Suspension Grade PVC
Used for paste resin, battery separator plate, and copolymer resin.
Emulsion Grade PVC
PVC

## Slide 8
India: Demand—Region
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2040F
East | 0.0954 | 0.1202 | 0.1201 | 0.1256 | 0.1138 | 0.1066 | 0.1123 | 0.1129
North | 0.2034 | 0.1972 | 0.1839 | 0.1824 | 0.1856 | 0.1865 | 0.1822 | 0.1822
South | 0.2756 | 0.2706 | 0.2737 | 0.2711 | 0.2747 | 0.2764 | 0.273 | 0.2705
West | 0.4256 | 0.412 | 0.4223 | 0.4209 | 0.4259 | 0.4305 | 0.4325 | 0.4344
India PVC Demand By Region, 2015-2040F
Total | 1,830 | 2,622 | 3,501 | 2,870 | 3,121 | 3,791 | 5,351 | 10,802
Source: TechSci Research
West India is the largest region
West India+South India : ~69% of the total demand
End-Use Sectors: infrastructure, agriculture, automotive, apparel, etc.
Hazira: RIL
Vadodara: RIL
Dahej: RIL
Dahej: RIL (Planned)
Dahej: OPaL (Upcoming)
4. Mundra: Adani (Planned)
5. Ratnagiri: Finolex
6. Kota: DCM Shriram
West
Paradip: IOCL (Planned)
East
Cuddalore: Chemplast
Cuddalore: Chemplast (Planned)
2. Mettur, Chemplast
3. Tuticorin, DCW Ltd.
South
1
2
3
4
6
5
1
1
2
3
PVC

## Slide 9
India: Imports, Exports (Opportunity)
Source: Department of Commerce, Ministry of Commerce and Industry, Government of India
India Trade Imports PVC:2021
Chart: 
| Japan | Taiwan | South Korea | USA
Imports | 412 | 271 | 212 | 77
Note: - The Import data is calculated for 2020 (calendar year from January 2020 to December 2020), India Import data vary as Import Export were taken from DGFT for Financial Year where FY 2021 means (April 2020 to March 2021).
Countries | 2020 |  | Net Export Potential
Countries | Import | Export | Net Export Potential
Bangladesh | 290.10 | 0 | 290.10
Malaysia | 169.66 | 47.62 | 122.04
Myanmar | 59.27 | 0 | 59.27
Sri Lanka | 45.9 | 0 | 45.9
Singapore | 36.87 | 2.35 | 34.52
Nepal | 6.99 | 0 | 6.99
Total Export Potential |  |  | 558.82
Anti-dumping duties imposed on imports from China PR and USA withdrawn in Feb 2022
India is the largest importer of PVC with 1.6 million tonnes of imports in 2020.
18% GST on PVC trade within the country
Suspension Grade PVC HS Code: 39041020
Emulsion Grade PVC HS Code: 39041010
PVC HS Code: 390410
10% custom duty imposed on Import
India is significantly (55%) imports dependent
Domestic Capacity Utilization : 89%
Significant Exports Opportunity in Nearby Countries
PVC
000’ Tonnes

## Slide 10
India: Pricing (Average) Trend
Source: TechSci Research
India PVC Suspension Ex- Mumbai Yearly Prices (FY 2013- FY 2021), USD/MT
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
PVC Suspension calendering grade K57 | 1079.4 | 1251.93 | 925.37 | 921.76 | 1140.8 | 1019.72 | 1133.32 | 1021.32 | 1327.77
PVC Suspension Semi rigid grade K67 | 1079.4 | 1207.69 | 906.67 | 896.46 | 1110.09 | 997.81 | 1097.83 | 1002.29 | 1264.55
PVC Suspension flexible grade K67 | 1036.77 | 1210.96 | 909.78 | 899.43 | 1117.76 | 997.81 | 1097.83 | 1000.27 | 1272.69
PVC Suspension rigid grade K67 | 1028.24 | 1202.77 | 901.99 | 891.99 | 1114.69 | 990.5 | 1120.97 | 996.9 | 1263.6
Factors impacting prices of PVC in India
Increase in demand from construction sector.
Import shortage and persistent hike in shipping charges across several trade routes along southeast Asia.
Persistent hike in shipping charges across several trade routes along Southeast Asia
Rise in demand from the agriculture sector in forthcoming crop season.
Revision in domestic price of PVC across the country, can impact downstream users negatively, as it may squeeze their margin.
Upward price trend is observed from 2020 Onwards
PVC price is primarily dependent on the fluctuating price of Ethylene/EDC/VCM
PVC

## Slide 11
Global: Capacity, Production
Global Polyvinyl Chloride (PVC) Capacity and Production, By Volume (000’ Tonnes), 2015 - 2030F
Chart: 
| 2015 | 2020 | 2021E | 2022F | 2025F | 2030F
Capacity | 53840 | 54960 | 54960 | 55560 | 56381 | 56381
Production | 40986.85 | 43090.14 | 43965.34 | 45332.21 | 47482.14 | 50444.82
Source: TechSci Research
Global Capacity by Company, By Volume- ((000’ tonnes)
Location | Companies | 2015 | 2020 | 2021E | 2022F | 2025F | 2030F
USA | Shin-Etsu, Formosa Plastics, Westlake, Occidental Petroleum, OxyVinyls, Georgia Gulf Corp | 9837 | 10157 | 10157 | 10157 | 10678 | 10678
China | Xinjiang Tianye Chemical, Xinjiang Huatai Heavy Chemical, Sinopec Qilu Petrochemical, Yibin Haifing Herui, Hanwha Chemical, Tianjin Dagu Chemical | 3560 | 3560 | 3560 | 3560 | 3560 | 3560
Germany | INOVYN, Vinnolit, VYNOVA | 1450 | 1450 | 1450 | 1450 | 1450 | 1450
France | INOVYN, Kem One, VYNOVA | 1445 | 1445 | 1445 | 1445 | 1445 | 1445
South Korea | LG Chem, Hanwha Chemical | 1380 | 1380 | 1380 | 1380 | 1380 | 1380
Others | Other Companies | 36168 | 36968 | 36968 | 37568 | 37878 | 37878
Total |  | 53840 | 54960 | 54960 | 55560 | 56391 | 56391
Asia Pacific is the largest demand generating region and holds around 40% of global capacity
India contributes ~3% of the global PVC capacity with 1,553 thousand tonnes of capacity in FY 2020
Shintech, Formosa Plastics, INOVYN, Occidental Petroleum, Westlake are top 5 PVC manufacturing companies globally (22% Capacity )
Rising demand for PVC in construction sector is anticipated to push the global demand for PVC
PVC

## Slide 12
Global: Demand
Source: TechSci Research
Global Polyvinyl Chloride (PVC) Demand, By Volume (000’ Tonnes), 2015-2030F
Chart: 
| 2015 | 2020 | 2021E | 2022F | 2025F | 2030F
By Volume (Thousand Tonnes) | 40986.85 | 43090.14 | 44908.54 | 46633.03 | 51632.61 | 60176.62
CAGR 2015-2020 | CAGR 2021E-2030F
1.01% | 3.31%
Global Polyvinyl Chloride Demand Supply Gap 2010-2040F (000’ Tonnes)
Parameters | 2010 | 2015 | 2020 | 2021E | 2025F | 2030F | 2040F
Capacity | 46604 | 53,840 | 54,960 | 54,960 | 56,381 | 56,381 | 56,381
Production | 33840 | 40,987 | 43,090 | 43,965 | 47,482 | 48,358 | 50,445
Demand | 33840 | 40,987 | 43,090 | 44909 | 51,633 | 60,177 | 80,097
Y-O-Y Growth Rate, % | - | - | -5.93% | 4.22% | 3.21% | 3.05% | 2.71%
Demand-Supply Gap | - | - | - | -943 | -4,150 | -9,732 | -29,652
Total | 40,987 | 43,090 | 44,908 | 46,635 | 51,632 | 60,177
Global Polyvinyl Chloride (PVC) Demand, By End Use, By Volume (000’ Tonnes), 2015–2030F
Chart: 
| 2015 | 2020 | 2021E | 2022F | 2025F | 2030F
Others | 0.1597 | 0.14724 | 0.14447 | 0.14161 | 0.13232 | 0.1139
Bottles | 0.0032 | 0.0054027 | 0.0059993 | 0.0066618 | 0.0091214 | 0.0154
Wires and Cables | 0.0745 | 0.07667 | 0.077111 | 0.077555 | 0.078902 | 0.0812
Profiles and Tubes | 0.152 | 0.15574 | 0.1565 | 0.15726 | 0.15957 | 0.1635
Films and Sheets | 0.1875 | 0.17895 | 0.17729 | 0.17564 | 0.17079 | 0.163
Pipe and Fittings | 0.4231 | 0.436 | 0.43863 | 0.44127 | 0.4493 | 0.463
India contributes ~8% of the PVC global demand at 3,501 thousand (FY2020)
India contributes to ~14% of the Global PVC pipes & fittings market demand (FY2020)
Vinnolit K GmbH / Krupp Uhde , Solvay Technology Solutions, Chisso, INEOS Technologies, The Geon Co., Vestolit GmbH / Hulls AG, and Hanwha are key technology providers for PVC for both grades (suspension and emulsion)
PVC

## Slide 13
Global: Demand
Source: TechSci Research
Region | Factors Impacting Demand
Asia-Pacific | Growing construction, healthcare, and packaging sector Initiatives and construction projects such as China Belt and Road Initiative, construction of new airports, and roads, “Housing for All’, “Smart Cities Project”, Industrial Corridor Project, “Make in India”. Increased manufacturing of blood and urine bags and other medical equipment as well during Covid-19.
North America | Construction and commercial activities High exports from USA. It is the largest PVC exporting country Increased industrial construction activities owing to shifting of manufacturing units back to USA Hindrance in supply chain Expansion of new PVC and VCM manufacturing plants Shintech, subsidiary of Japan’s Shin-Etsu Chemical Co. has invested USD1.3 billion to expand its PVC manufacturing facilities at its Plaquemine, LA., site with an installed capacity of 380 thousand tonnes of PVC and 580 KTPA for the manufacturing of its precursor VCM. Formosa is scheduled to start a new 130 KTPA PVC production line at its Baton Rouge, LA plant in the 4th quarter 2022.
Europe | Growth in construction activities coupled with increase in demand from automotive sector Supply chain disruption Volatile prices due to shortage of supply of PVC Increasing demand for pipes, profiles, insulating materials
MEA and South America | Multiple large scale infrastructure projects in MEA Increasing usage of PVC pipes, cables and window profiles in housing, building and other infrastructural developments. Heavy investment in downstream sector in South America
Global Polyvinyl Chloride (PVC) Demand, By Region, By Volume (000’ Tonnes), 2015–2030F
Chart: 
| 2015 | 2020 | 2021E | 2022F | 2025F | 2030F
South America | 0.0755 | 0.078 | 0.062 | 0.0612 | 0.0586 | 0.0544
Middle East & Africa | 0.0844 | 0.0862 | 0.0872 | 0.0864 | 0.0872 | 0.0898
Europe | 0.1012 | 0.10524 | 0.10544 | 0.1056 | 0.1032 | 0.0971
North America | 0.11148 | 0.11007 | 0.11036 | 0.10962 | 0.10601 | 0.10122
Asia-Pacific | 0.6274 | 0.6205 | 0.635 | 0.6372 | 0.645 | 0.6575
Total | 40,987 | 43,090 | 44,908 | 46,635 | 51,632 | 60,177
“Atmanirbhar Bharat” and “Make in India” policies are driving the domestic production
PVC

## Slide 14
Financial Analysis: Plant Set-up
PVC

## Slide 15
Plant Set-up: Capex
Total Fixed Capital Investment: INR 4,058 Crore
Total Capital Investment: INR 4,159 Crore
Option:1
Total Fixed Capital Investment: INR 4,443 Crore
Total Capital Investment: INR 6,053 Crore
Option:2
Chart: 
| Total Direct Plant Cost | Total indirect Plant Cost
Total Fixed Capital Investment | 3004 | 1054
Chart: 
| Total Fixed Capital Investment | Working Capital
Total Capital Investment | 4058 | 101
Chart: 
| Total Direct Plant Cost | Total indirect Plant Cost
Total Fixed Capital Investment | 3288.6 | 1154
Chart: 
| Total Fixed Capital Investment | Working Capital | Open Jetty Facility for Ethylene, EDC and VCM Import
Total Capital Investment | 4442.5 | 111 | 1500
Total Fixed Capital Investment: INR 2,415 Crore
Total Capital Investment: INR 4,428 Crore
Option:3
Chart: 
| Total Direct Plant Cost | Total indirect Plant Cost
Total Fixed Capital Investment | 1852 | 563
Chart: 
| Total Fixed Capital Investment | Working Capital | Open Jetty Facility for EDC and VCM Import
Total Capital Investment | 2415 | 63 | 1950
350 KTPA PVC + Captive Ethylene
500 KTPA PVC (350 KTPA (captive ethylene)+150 KTPA(EDC / VCM Outsourced)
500 KTPA EDC / VCM to PVC, EDC / VCM Outsourced
PVC

## Slide 16
Plant Set-up: Opex
Total Production Cost INR 1,256 Crore
Total Variable Cost: INR 1,082 Crore
Option:1
Total Production Cost : INR 1,937 Crore
Total Variable Cost: INR 1,686 Crore
Option:2
Chart: 
| Variable | Fixed
Column1 | 1160 | 96
Chart: 
| Raw Materials | Cat-Chem | Others
Total Capital Investment | 822 | 102 | 157
Chart: 
| Variable | Fixed
Total Fixed Capital Investment | 1807 | 131
Chart: 
| Raw Material | Cat-Chem | Others
Total Capital Investment | 1378 | 111 | 197
Total Production Cost : INR 2,877 Crore
Total Variable Cost: INR 2,673 Crore
Option:3
Chart: 
| Variable | Fixed
Total Fixed Capital Investment | 2779 | 98
Chart: 
| Raw Material | Cat-Chem | Others
Total Capital Investment | 2417.6 | 110.7 | 144
350 KTPA PVC + Captive Ethylene
500 KTPA PVC (350 KTPA (Captive Ethylene)+150 KTPA(EDC / VCM Outsourced)
500 KTPA EDC / VCM to PVC, EDC / VCM Outsourced
PVC
Others include Variable and Selling Overheads

## Slide 17
Plant Set-up: Operating Revenue, Operating Cost, Gross Margin
Source: TechSci Research
Operating Revenue
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 | 1831.363 | 3094.3312 | 4039 | 5414 | 7161.7448
Option-2 | 2616.2328 | 4420.4732 | 5847.265 | 7734.5809 | 10231.064
Option-3 | 2616.2328 | 4420.4732 | 5847.265 | 7734.5809 | 10231.064
Note: All figures are in INR Crores
Operating Cost
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 | 978 | 1481 | 1940 | 2521 | 3286
Option-2 | 1569 | 2408 | 3149 | 4135 | 5405
Option-3 | 2118.5681 | 3393.8448 | 4470.587 | 5891.2152 | 7766.1353
Gross Margin
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 | 853 | 1614 | 2153 | 2893 | 3875
Option-2 | 1048 | 2012 | 2698 | 3600 | 4826
Option-3 | 497.6647 | 1026.6284 | 1376.6779 | 1843.3657 | 2464.9288
Note: All figures are in INR Crores
Note: All figures are in INR Crores
Option 1:Lower operating revenue because of lower capacity
Option 2 & 3 : Same operating revenue because both has the same capacity
Option 1 :Inhouse production of feedstock offers an advantage of lowest operating cost
Option 2 & 3 :Higher operating cost because of higher capacity and EDC/VCM outsourcing.
Gross Margins in option 1 and 2 are improved in comparison to 3, because of the spread between PVC and EDC / VCM.
350 KTPA PVC + Captive Ethylene
500 KTPA PVC (350 KTPA (Captive Ethylene)+150 KTPA(EDC / VCM Outsourced)
500 KTPA EDC / VCM to PVC, EDC / VCM Outsourced
PVC

## Slide 18
Plant Set-up: Summary
Source: TechSci Research
Chart: 
| Total CAPEX | NPV | Gross Revenue | OPEX
Option-1 | 4159.45 | 12736 | 3094.33 | 1481
Option-2 | 6053.45 | 15080 | 4420.47 | 2408
Option-3 | 4420 | 6440 | 4420 | 3394
All values are in INR Crores
Project Sensitivity Analysis | Project Sensitivity Analysis | 
S.No. | Project Sensitivity | Profit After Tax
 |  | Option-1
 | Profit After Tax (at optimum capacity utilization) | Nil
1 | Selling Price decreases by 11%, Raw Material Price remains same | 20% decrease
2 | Increase in Raw Material price by 16.5 % with no change in selling price | 14% decrease
3 | Increase in raw material price by 9 % with decrease in selling price by 5% | 20% decrease
4 | Increase in Cost of Production by 14.5% with no change in selling price | 18% decrease
PVC
350 KTPA PVC + Captive Ethylene
500 KTPA PVC (350 KTPA (Captive Ethylene)+150 KTPA(EDC / VCM Outsourced)
500 KTPA EDC / VCM to PVC, EDC / VCM Outsourced

## Slide 19
Source: Department of Commerce, Ministry of Commerce and Industry, Government of India
Note: - The Import data is calculated for 2020 (calendar year from January 2020 to December 2020), India Import data vary as Import Export were taken from DGFT for Financial Year where FY 2021 means (April 2020 to March 2021).
Plant Set-up: Raw Material Availability—Relevant To Option 2 and Option 3
India Trade Import Details of VCM (2020), (000’ Tonnes)
India Trade Import Details of EDC (2020), (000’ Tonnes)
Chart: 
| Saudi Arabia | USA | Qatar | South Korea
Imports | 336 | 172 | 122 | 61
Chart: 
| Qatar | Japan | France | Indonesia
Imports | 300 | 83 | 49 | 19
India Net VCM Import: 461 (000’ Tonnes)
India Net EDC Import: 725 (000’ Tonnes)
Option 2: 500 KTPA PVC (350 KTPA from captive ethylene and 150 KTPA Through EDC / VCM Outsourced)
Option 3: 500 KTPA EDC / VCM to PVC, EDC / VCM Outsourced
Northeast Asia held the largest share: Production and consumption
EDC/VCM is primarily used to manufacture PVC Resin
EDC (Captive Production in India): Reliance
VCM (Captive Production in India): Reliance, Finolex, Chemplast, DCW
VCM and EDC have to be sourced from Imports : Option 2 and Option 3
000’ Tonnes
000’ Tonnes
PVC

## Slide 20
Recommendations & Conclusions
PVC

## Slide 21
Conclusions & Recommendations: Market Opportunity
All manufactures offer suspension grade
Finolex Industries Limited & Chemplast Sanmar Limited also offer emulsion grade
Upcoming Greenfield / Brownfield Projects will intensity the competition
Demand-Supply Gap (1733 KT in 2022 to 6752 KT in 2040) arguments the need for new player , even post-realization of ongoing/ upcoming Greenfield/ Brownfield Projects
Suspension Grade will always be the most prominent type :95% Demand
Pipes & Fittings will always be the most prominent end-use :73% Demand
Rigid PVC will always be is the most prominent type :85% Demand
West India+ South India will Continue to be the largest region: 70% Demand
Domestic Capacity Utilization: 89%
Overall, the PVC market will be more than approximately three times from 2870 Thousand MT in 2021 to 10,802 Thousand MT in 2040
Significant Exports Opportunity in Nearby Countries
India is significantly (55%) imports dependent
PVC price is primarily dependent on the fluctuating price of Ethylene / EDC/VCM
A substantial business opportunity exists, but there would always be a threat of new players entering the market, specifically those companies with the advantage of in-house Ethylene. The early entrant will influence the entry plans of possible another entrant.
OPAL can utilize a fully integrated unit to advantage as it has captive ethylene.
RIL—significant competitor: dedicated plants in Hazira. Vadodara. Also, expansion plans.
RIL Dahej unit is planning to add 1000 KTPA capacity in near vicinity which may result in oversupply condition in western region acting as a threat for OPaL.
PVC
Strategic location plays a vital role for OPaL, as the availability of chlorine is a significant challenge for players operating in the market. Therefore, OPaL can go for a long-term contract with caustic soda players operating in the region for the availability of chlorine. Gujarat Alkalies and Chemicals Limited, Meghmani Organics Limited and DCM Shriram Consolidated Limited are the leading players in the region.
Vinnolit K GmbH / Krupp Uhde (Low Cost of Production) , INEOS Technologies( Higher Yield), and Hanwha (All Grades) are recommended Technology Licensors

## Slide 22
Conclusions & Recommendations: Most Suitable Plant Set-up Option
Features | Option 1 | Option 2 | Option 3
CapEx (INR Crore) | 4159 | 6053 | 4427
OpEx (INR Crore) | 1256 | 1938 | 2877
NPV (INR Crore) | 12735 | 15080 | 6440
IRR | 19.40% | 16.96% | 11.95%
Payback Period (Years) Simple | 3.32 | 3.77 | 5.05
Propane (Raw material & Feed) | Propane through Parent Company ONGC | Propane through Parent Company ONGC | Not required
EDC/ VCM (Raw material & Feed) | Not Required | Required through Imports: 150KTPA | Required through Imports 500 KTPA
Chlorine Sourcing | Chlor-Alkali units (DCM Sriram, Meghmani, GACL) in proximity | Chlor-Alkali units (DCM Sriram, Meghmani, GACL) in proximity | Not Required
Jetty Facility | Not Required | Required | Required
Margin %(Starting from First Year of Operation | 48.59% | 40.04% | 19.02%
Preference Option Rank:
350 KTPA PVC + Captive Ethylene
500 KTPA PVC (350 KTPA (captive ethylene)+150 KTPA(EDC / VCM Outsourced)
500 KTPA EDC / VCM to PVC, EDC / VCM Outsourced
1
2
3
OPaL will have sufficient ethylene, propylene and benzene after commissioning the propane furnace. Therefore, Option 1 will have better NPV, IRR, Payback Period and margin despite having the highest CapEx
The Option1 is most feasible in terms of execution and realization as it won’t require EDC/VCM sourcing from the international market. The jetty facility will also be not needed.
PVC

## Slide 23
Phenol

## Slide 24
India: Manufacturing Landscape
Source: TechSci Research
Dahej, Deepak Phenolics
Navi Mumbai, SI Group India
West
Kochi, Hindustan Organic Chemicals Ltd.
South
India Phenol Capacity, By Company (000’ Tonnes)
Company | Technology Provider | Capacity, FY2021
Deepak Phenolics Ltd. | Kellogg Brown & Root International Inc. (KBR) (For Phenol and Acetone) Honeywell UOP LLC (Cumene) | 200
Hindustan Organic Chemicals Ltd. | Honeywell UOP LLC | 42
SI Group India Ltd. | Honeywell UOP LLC | 37
1
2
1
Phenol
Deepak Phenolics has integrated unit to produce IPA from Acetone
Deepak Phenolics has capacity of Cumene (captive consumption)

## Slide 25
Parameters | 2010 | 2015 | 2021 | 2022E | 2025F | 2030F | 2035F | 2040F
Capacity | 45.00 | 45.00 | 169.00 | 169.00 | 169.00 | 169.00 | 169.00 | 169.00
Production | 44.00 | 26.00 | 149.00 | 152.00 | 155.00 | 164.00 | 165.00 | 165.00
Import | 80.00 | 127.00 | 82.00 | 101.00 | - |  |  | 
Export | 0.50 | 3.18 | 28.16 | 34.00 |  |  |  | 
Inventory | 0.89 | 0.52 | 2.99 | 3.03 |  |  |  | 
Demand | 123.00 | 149.00 | 200.00 | 216.00 | 262.00 | 358.00 | 474.00 | 605.00
Y-O-Y Growth Rate, % | - | 3.49% | 3.18% | 8.05% | 6.22% | 6.88% | 5.52% | 4.71%
Demand - Supply Gap |  |  |  | -65 | -106 | -194 | -309 | -440
India: Capacity, Production, Demand
Source: TechSci Research
India Phenol Demand Supply Scenario, 2010-2040F (000 Tonnes)
Parameters | 2010 | 2015 | 2021 | 2022E | 2025F | 2030F | 2035F | 2040F
Capacity | 79.00 | 79.00 | 279.00 | 279.00 | 279.00 | 279.00 | 279.00 | 279.00
Production | 71.82 | 42.12 | 246.90 | 250.70 | 257.35 | 271.05 | 273.42 | 273.42
Import | 112.40 | 199.68 | 170.62 | 148.73 |  |  |  | 
Export | 0.40 | 1.50 | 51.05 | 44.65 |  |  |  | 
Inventory | 4.50 | 3.12 | 4.94 | 2.56 |  |  |  | 
Demand | 179.00 | 237.00 | 362.00 | 352.00 | 429.00 | 584.00 | 811.00 | 1136.00
Y-O-Y Growth Rate, % |  | 2.99% | 9.91% | -2.58% | 6.50% | 6.80% | 6.90% | 7.01%
Demand - Supply Gap |  |  |  | -102 | -171 | -313 | -537 | -863
India Acetone Demand Supply Scenario, 2010-2040F (000 Tonnes)
India Phenol Capacity and Production, By Volume (000’ Tonnes), 2010 - 2040F
Chart: 
| 2010 | 2015 | 2017 | 2019 | 2020 | 2021 | 2022E | 2025F | 2030F | 2035F | 2040F
Capacity | 79 | 79 | 79 | 279 | 279 | 279 | 279 | 279 | 279 | 279 | 279
Production | 71.82 | 42.12 | 43.54 | 83.52 | 223.6 | 246.9 | 250.7 | 257.35 | 271.05 | 273.42 | 273.42
Phenol
Demand-Supply Gap arguments the need of a new player . No explanation /New plant announced, as of now.
Downstream integration opportunities exist to produce chemical like Bisphenol A, Isopropyl Alcohol, Ketoxime etc.
Well Established technology and production of cumene as intermediate and Acetone as by product add to volume and additional revenues in this segment.
Significant Imports: 42% Demand

## Slide 26
India: Demand—Phenol
India Phenol Demand, By End Use, By Volume (000’ Tonnes), FY 2010– FY 2040F
Source: TechSci Research
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2035F | 2040F
Others | 0.1456 | 0.148 | 0.1355 | 0.1567 | 0.1391 | 0.1354 | 0.1289 | 0.1275 | 0.1258
Bisphenol-A | 0.0498 | 0.0509 | 0.0935 | 0.1063 | 0.1082 | 0.1141 | 0.1239 | 0.1255 | 0.1274
Pharmaceuticals | 0.082 | 0.0984 | 0.1245 | 0.1757 | 0.129 | 0.1261 | 0.1212 | 0.1235 | 0.1253
Phenol Formaldehyde Resin | 0.7226 | 0.7027 | 0.6465 | 0.5613 | 0.6237 | 0.6244 | 0.626 | 0.6235 | 0.6215
Total | 179 | 237 | 329 | 362 | 352 | 429 | 584 | 811 | 1136
Others include Caprolactam, Aniline, Cyclohexanone, etc
India Phenol Demand, By Volume (000’ Tonnes), 2010-2040F
Chart: 
| 2010 | 2015 | 2017 | 2019 | 2020 | 2021 | 2022E | 2025F | 2030F | 2035F | 2040F
By Volume (Thousand Tonnes) | 179.32 | 245.33 | 307.34 | 300.46 | 328.92 | 361.532 | 352.22 | 428.75 | 584.49 | 810.76 | 1136.39
CAGR 2010-2021 | CAGR 2022E-2030F | CAGR 2031F-2040F
6.58% | 6.54% | 6.91%
Phenol Formaldehyde Resin is the most prominent end-use
Major players are Deepak Phenolics Ltd, Hindustan Organic Chemicals Ltd. and SI Group India Ltd.
Phenol Formaldehyde resin accounts to nearly 70% of the total demand in India
Growing demand of Bisphenol- A is one of the major drivers
Honeywell UOP, The Kellogg Brown & Root (KBR) Technology, Lummus Phenol Technology, Badger Acetone -to- Cumene (ATC) Technology are the major technology providers for Phenol and Acetone manufacturing
Phenol

## Slide 27
Total | 179 | 237 | 329 | 362 | 352 | 429 | 584 | 811 | 1136
India: Demand—Phenol
Source: TechSci Research
India Phenol Demand, By Region, By Volume (000’ Tonnes), FY 2010– FY 2040F
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022E | 2025F | 2030F | 2035F | 2040F
East | 0.0526 | 0.0611 | 0.0678 | 0.069 | 0.0695 | 0.0726 | 0.0763 | 0.0751 | 0.0759
North | 0.083 | 0.0921 | 0.0981 | 0.0992 | 0.0996 | 0.1028 | 0.1064 | 0.1081 | 0.1094
South | 0.2821 | 0.272 | 0.278 | 0.2791 | 0.2798 | 0.2825 | 0.2861 | 0.288 | 0.2897
West | 0.5823 | 0.5748 | 0.5561 | 0.5527 | 0.5511 | 0.5421 | 0.5312 | 0.5288 | 0.525
Dahej, Deepak Phenolics
Navi Mumbai, SI Group India
West
Kochi, Hindustan Organic Chemicals Ltd.
South
1
2
1
West India is the largest region
West India+South India: ~83% of the total demand
End-Use Sectors : Pharmaceuticals and construction
Phenol

## Slide 28
India Acetone Demand, By Market Share, By Region, FY2021 & FY2040 (%)
Source: TechSci Research
India Acetone Demand, By Market Share, By Region, FY2040 (%)
Chart: 
| West | South | North | East
2040 | 0.4372 | 0.3395 | 0.1663 | 0.057
India Acetone Demand, By Market Share, By Region, FY2021 (%)
Chart: 
| West | South | North | East
2019 | 0.4892 | 0.305 | 0.1575 | 0.0483
West
East
South
North
India: Demand—Acetone
End Use | FY 2021 | FY 2040
Pharmaceuticals & Solvent | 61.46% | 55.23%
Bisphenol-A (BPA) | 12.04% | 16.83%
Methyl Methacrylate (MMA) | 11.55% | 10.48%
Methyl Isobutyl Ketone (MIBK) | 10.10% | 11.59%
Others | 4.85% | 5.87%
India Acetone Demand, By End Use, By Volume (000’ Tonnes), FY 2021, FY 2040F
South India is second largest because of growing Pharmaceuticals industry and Production Linked Incentive (PLI) scheme to encourage the pharmaceutical industry growth.
Phenol
West India+South India: ~80% of the total demand
West India is the largest region

## Slide 29
India: Trade, Exports (Opportunity)
Export Potential Market of Phenol
Countries | 2020 |  | 
 | Import | Export | Net Export Potential
China | 709.92 | 17.29 | 692.63
Taiwan | 105.56 | 180.52 | -74.96
Thailand | 40.08 | 225.11 | -185.03
Malaysia | 22.73 | 0.25 | 22.48
Indonesia | 17.14 | 0.27 | 16.87
Note: Import and export volumes are in thousand tonnes
Source: - Department of Commerce, Ministry of Commerce and Industry, Government of India, UN Comtrade
Present Scenario of Anti-Dumping Duty (ADD)
Countries | Quantum of Duty imposed | Remarks
USA | USD 250 per MT - USD 350 per MT | 
Thailand | USD 250 per MT - USD 350 per MT | 
South Korea | US$ Nil to 253.06 per MT | Removed effective from 31/10/2021
European Union | US$ Nil to 253.06 per MT | Removed effective from 31/10/2021
Singapore | US$ Nil to 253.06 per MT | Removed effective from 31/10/2021
18% GST on Phenol traded within the country
7.5% custom duty imposed on Import
10% social welfare surcharge on Phenol
Phenol HS Code: 29071110
Antidumping duty levied on imports of Phenol from Thailand and USA
India may be a significant exporter of Phenol and Acetone. OPaL can replicate the exports business model of Deepak Phenolics (Only Exporter) and, in the proximity of OPaL
Phenol
Significant Exports Opportunity in Nearby Countries

## Slide 30
India: Pricing (Average) Trend
Source: TechSci Research
India Phenol & Acetone Historical prices (FY 2013-FY 2022) (USD/MT)
Chart: 
| FY 2013 | FY 2014 | FY 2015 | FY 2016 | FY 2017 | FY 2018 | FY 2019 | FY 2020 | FY 2021 | FY 2022
Phenol | 1881.63 | 1727.25 | 1521.88 | 1282.18 | 1278.65 | 1361.92 | 1373.33 | 1088.12 | 1115.6 | 1586.93
Acetone | 871.738 | 807.4137 | 673.0559 | 557.2258 | 757.2174 | 764.6113 | 644.4192 | 542.5101 | 752.3745 | 944.96
Upward price trend is observed from 2021 onwards
Phenol
Phenol price is primarily dependent on the fluctuating price of Propylene, Benzene and Cumene
Acetone price is driven by market conditions and production of phenol

## Slide 31
Global: Capacity, Production
Global Phenol Capacity and Production, By Volume (000’ Tonnes), 2010 - 2040F
Chart: 
| 2010 | 2015 | 2017 | 2019 | 2020 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
Capacity | 9450 | 10223 | 11873 | 12523 | 12523 | 12523 | 12523 | 13523 | 13773 | 13773 | 13773
Production | 7957 | 8407.8368 | 8880.09 | 9562.8633 | 10194.371 | 10864.631 | 11007.397 | 11915.8701 | 12665.19 | 12756.86 | 12757
Source: TechSci Research
INEOS Group, Cepsa Corporation, Kumho Chemicals, LG Chem are the leading global producers of Phenol.
Ineos group operates phenol and acetone plants at sites in Gladbeck, Germany; Antwerp, Belgium; and Mobile, Alabama in the United States. All three sites use their own proprietary technology.
  In Europe, the major competitors for Ineos group are Cepsa, Novapex, Borealis and Versalis.
  In North America, major competitors are Shell and Honeywell.
  Has consumers globally, including Covestro (previously Bayer), Olin (previously Dow), Sabic, Fibrant (previously DSM), Evonik and Lucite.
India contributes ~2% of the global phenol capacity in FY2020
Phenol

## Slide 32
Global: Capacity, Production
Capacity by Location, 000’ Tonnes
Source: TechSci Research
Location | Companies | 2010 | 2015 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
USA | Ineos Group Ltd, Advansix, Shell Chemicals, SABIC Innovative Plastics, Altivia Petrochemicals, Olin Corporation, Georgia Gulf Corporation | 2422 | 2422 | 2572 | 2572 | 2882 | 2882 | 2882 | 2882
China | Ineos Group Ltd, Cepsa Corporation, Zhejiang Rongsheng, Chang Chun Chemical, Shanghai Sinopec Mitsui, CNOOC Huizhou | 250 | 800 | 1820 | 1820 | 1820 | 1820 | 1820 | 1820
South Korea | Kumho P&B Chemicals., Inc., LG Chem | 980 | 980 | 1280 | 1280 | 1280 | 1280 | 1280 | 1280
Taiwan | Formosa Chemical and Fibre, Taiwan Prosperity Chemical Corp., Chang Chun Plastic | 960 | 960 | 960 | 960 | 1060 | 960 | 960 | 960
Belgium | Ineos Group Ltd | 680 | 680 | 680 | 680 | 680 | 680 | 680 | 680
Others |  | 4158 | 4381 | 5211 | 5211 | 5801 | 6151 | 6151 | 6151
Total |  | 9450 | 10223 | 12523 | 12523 | 13523 | 13773 | 13773 | 13773
Major Expansions for the Manufacturing of Cumene, Phenol and Acetone, By Location
Company | Licensor | Product | Capacity (000’ Tonne) | Location | Likely Year of Commissioning
Formosa Chemicals and Fibre Corp | Lummus Technology | Cumene, Phenol & Acetone | 400 | Nimbo, China | 2025
PKN Orlen | UOP’s Q-Max | Cumene, Phenol & Acetone | 200 | Plock, Poland | 2024
PKN Orlen | Badger | Acetone and Isopropanol | 140 | Plock, Poland | 2024
Reliance Industries Ltd | NA | Cumene, Phenol & Acetone | 200 | Jamnagar, Gujarat | Planning Stage Only
Ineos Group | Ineos | Cumene | 750 | Marl, Germany | 2022
Haiwan Chemical | KBR | Cumene, Phenol & Acetone | 320 | Shandong, China | 2024
Phenol

## Slide 33
Global: Demand- Phenol
Source: TechSci Research
Global Phenol Demand Supply Scenario, 2010-2040F, (000 Tonnes)
Parameters | 2010 | 2015 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
Capacity | 10,223.00 | 10,223.00 | 12,523.00 | 12,523.00 | 13,523.00 | 13,773.00 | 13,773.00 | 13,773.00
Production | 7,956.00 | 8,408.00 | 10,865.00 | 11,007.00 | 11,916.00 | 12,665.00 | 12,757.00 | 12,757.00
Demand | 7,956.24 | 8,407.84 | 10,828.50 | 11,267.00 | 12,697.00 | 15,258.20 | 17,819.20 | 20,527.31
Y-O-Y Growth Rate, % |  | 4.99% | 6.22% | 4.05% | 3.82% | 3.39% | 3.36% | 2.80%
Demand - Supply Gap |  |  | 36.00 | -260.00 | -781.00 | -2,593.00 | -5,062.00 | -7,770.00
Global Phenol Demand, By Volume (000’ Tonnes), 2010-2040F
Chart: 
| 2010 | 2015 | 2017 | 2019 | 2020 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
By Volume (Thousand Tonnes) | 7956.24 | 8407.84 | 8880.09 | 9562.86 | 10194.36 | 10128.46 | 11267.01 | 12696.97 | 15258.16 | 17819.23 | 20527
CAGR 2010-2021 | CAGR 2022E-2030F | CAGR 2031F-2040F
3.1% | 3.9% | 3.0%
India contributes~3% of the global phenol market demand (FY2020)
Growth in construction, automotive and infrastructure sectors supports phenol demand
Phenol

## Slide 34
Chart: 
| 2010 | 2015 | 2020 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
South America | 0.0439 | 0.0619 | 0.0455 | 0.0372 | 0.0333 | 0.0356 | 0.0407 | 0.033 | 0.042
Middle East & Africa | 0.0615 | 0.0572 | 0.0682 | 0.0691 | 0.0672 | 0.0691 | 0.0612 | 0.0655 | 0.0671
North America | 0.165 | 0.1705 | 0.1604 | 0.1662 | 0.1705 | 0.1693 | 0.1723 | 0.1655 | 0.1553
Europe | 0.2124 | 0.2 | 0.1975 | 0.197 | 0.1965 | 0.188 | 0.1786 | 0.1755 | 0.1684
Asia-Pacific | 0.5172 | 0.5104 | 0.5284 | 0.5305 | 0.5325 | 0.538 | 0.5472 | 0.5605 | 0.5672
Global: Demand- Phenol
Source: TechSci Research
Global Phenol Demand, By End Use, By Volume (000’ Tonnes), 2010–2040F
Chart: 
| 2010 | 2015 | 2020 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
Others | 0.04 | 0.069728 | 0.064632 | 0.066075 | 0.065411 | 0.062917 | 0.058354 | 0.0565 | 0.0656
Pharmaceuticals | 0.1311 | 0.12499 | 0.1322 | 0.13302 | 0.13433 | 0.13914 | 0.14574 | 0.146 | 0.1484
Phenolic Resin | 0.3474 | 0.33928 | 0.34588 | 0.34508 | 0.34485 | 0.34446 | 0.34205 | 0.3425 | 0.3381
Bisphenol-A | 0.4815 | 0.466 | 0.45729 | 0.45583 | 0.45541 | 0.45349 | 0.45385 | 0.455 | 0.4479
Total | 7956.24 | 8407.84 | 10194.37 | 10828.46 | 11267.01 | 12696.97 | 15258.16 | 17819.23 | 20527.31
Global Phenol Demand, By Region, By Volume (000’ Tonnes), 2010–2040F
Total | 7956.24 | 8407.84 | 10194.37 | 10828.46 | 11267.01 | 12696.97 | 15258.16 | 17819.23 | 20527.31
Bisphenol-A is the most prominent end-use
Asia-Pacific is the most prominent region
Manufacturing of polycarbonate and epoxy resin is expected to drive the Bisphenol A (BPA) demand
India contributes ~6% of the APAC phenol market demand in FY2020
Epoxy resins are used manufacturing in adhesives, fillings, and composite materials.
Phenolic Resin is the largest derivative in the APAC region, holding approximately 41% of total consumption
Phenolic resins are widely used as a binding and insulating material
India contributes~1% of the global BPA market demand (FY2020)
Phenol

## Slide 35
Global: Demand- Acetone
Source: TechSci Research
Global Acetone Demand Supply Scenario, 2010-2040F, (000’ Tonnes)
Parameters | 2010 | 2015 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
Capacity | 5084.4 | 6265.8 | 7513.8 | 7513.8 | 8113.8 | 8263.8 | 8263.8 | 8263.8
Production | 4973.9 | 5872.7 | 7790.2 | 8175.5 | 9256.8 | 11248.4 | 13516.8 | 16083.9
Demand | 4973.9 | 5872.7 | 8134.9 | 8587.2 | 10176.5 | 13094.7 | 16563.4 | 20235.0
Y-O-Y Growth Rate, % |  | 4.64% | 6.12% | 5.56% | 5.94% | 4.94% | 4.72% | 3.72%
Demand - Supply Gap |  |  | -344.7 | -411.8 | -919.7 | -1846.3 | -3046.6 | -4151.1
Global Acetone Demand, By Volume (000’ Tonnes), 2010-2040F
Chart: 
| 2010 | 2015 | 2017 | 2019 | 2020 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
By Volume (Thousand Tonnes) | 4973.897 | 5872.6778 | 6323.5207 | 6931.5926 | 7665.7906 | 8134.937 | 8587.2395 | 10176.476 | 13094.6666 | 16563.3838 | 20235.0257
CAGR 2010-2021 | CAGR 2022E-2030F | CAGR 2031F-2040F
4.6% | 5.4% | 4.4%
India contributes~2% of the global acetone market demand (FY2020)
Growth in pharmaceutical, automotive and solvent based products like thinners supports phenol demand
Phenol

## Slide 36
Chart: 
| 2010 | 2015 | 2020 | 2021E | 2022F | 2025F | 2030F | 2035F | 2040F
South America | 0.031326 | 0.029482 | 0.027593 | 0.028279 | 0.027715 | 0.027173 | 0.027173 | 0.026483 | 0.025753
Middle East & Africa | 0.057142 | 0.054249 | 0.051957 | 0.053249 | 0.052188 | 0.051166 | 0.051166 | 0.049866 | 0.048492
North America | 0.26384 | 0.24701 | 0.26688 | 0.25096 | 0.24597 | 0.2378 | 0.2378 | 0.23042 | 0.22413
Europe | 0.27685 | 0.2562 | 0.21018 | 0.19437 | 0.19011 | 0.18699 | 0.18699 | 0.18355 | 0.17953
Asia-Pacific | 0.37084 | 0.41306 | 0.4434 | 0.47314 | 0.48401 | 0.49687 | 0.49687 | 0.50969 | 0.52209
Global: Demand- Acetone
Source: TechSci Research
Global Acetone Demand, By End Use, By Volume (000’ Tonnes), 2021 & 2040F
Global Acetone Demand, By Region, By Volume (000’ Tonnes), 2010–2040F
Total | 4973.9 | 5872.7 | 7665.8 | 8134.9 | 8587.2 | 10176.5 | 13094.7 | 16563.4 | 20235.0
Pharmaceuticals & Solvent is the most prominent end-use
Asia-Pacific is the most prominent region
Manufacturing of Bisphenol-A and IPA will drive the future demand
India contributes ~5% of the APAC acetone market demand in FY2022
In China and India, Acetone is used for the manufacturing of vitamins API and antibiotics (cephalosporins).
China contributes~18% of the global acetone market demand (FY2020)
Phenol
End Use | 2021 | 2040
Pharmaceuticals & Solvent | 40.61% | 42.03%
Bisphenol-A (BPA) | 24.85% | 22.13%
Methyl Methacrylate (MMA) | 14.63% | 16.15%
Methyl Isobutyl Ketone (MIBK) | 12.71% | 11.43%
Others | 7.20% | 8.26%

## Slide 37
Financial Analysis: Plant Set-up
Phenol

## Slide 38
Plant Set-up: Capex
Total Fixed Capital Investment: INR 1,568Crore
Total Capital Investment: INR 1,769 Crore
Option-1
Total Fixed Capital Investment: INR 1,392 Crore
Total Capital Investment: INR 1,549 Crore
Chart: 
| Total Direct Plant Cost | Total indirect Plant Cost
Total Fixed Capital Investment | 1132.3 | 436
Chart: 
| Total Fixed Capital Investment | Working Capital | OSBL facilities
Total Capital Investment | 1568 | 42 | 159
Chart: 
| Total Direct Plant Cost | Total indirect Plant Cost
Total Fixed Capital Investment | 1000 | 392
Chart: 
| Total Fixed Capital Investment | Working Capital | OSBL facilities
Total Capital Investment | 1392 | 37 | 120
Total Fixed Capital Investment: INR 1,671 Crore
Total Capital Investment: INR 1,937 Crore
Chart: 
| Total Direct Plant Cost | Total indirect Plant Cost
Total Fixed Capital Investment | 1207 | 464
Chart: 
| Total Fixed Capital Investment | Working Capital | Gantry and OSBL Facilities
Total Capital Investment | 1671 | 45 | 222
Option:2
Option:3
200 KTPA Phenol+120 KTPA Acetone (Propane Furnace Additional)
200 KTPA Phenol + 120 KTPA Acetone, (with available propylene and benzene)
200 KTPA Phenol + 120 KTPA Acetone, (Propylene : 80 % In-house+ 20 % external)
Phenol

## Slide 39
Plant Set-up: Opex
Total Production Cost : INR 1, 681 Crore
Total Variable Cost: INR 1,674 Crore
Option:1
Total Production Cost : INR 1,360 Crore
Total Variable Cost: INR 1,308 Crore
Option:2
Chart: 
| Variable | Fixed
Column1 | 1624 | 57
Chart: 
| Raw Materials | Cat-Chem | Others
Total Capital Investment | 1250 | 94 | 280
Chart: 
| Variable | Fixed
Total Fixed Capital Investment | 1308 | 52
Chart: 
| Raw Material | Cat-Chem | Others
Total Capital Investment | 992 | 76 | 240
Total Production Cost : INR 1,756 Crore
Total Variable Cost: INR 1,630 Crore
Option:3
Chart: 
| Variable | Fixed
Total Fixed Capital Investment | 1700 | 56
Chart: 
| Raw Material | Cat-Chem | Others
Total Capital Investment | 1327 | 94 | 279
200 KTPA Phenol+120 KTPA Acetone (Propane Furnace Additional)
200 KTPA Phenol + 120 KTPA Acetone, (with available propylene and benzene)
200 KTPA Phenol + 120 KTPA Acetone, (Propylene : 80 % In-house+ 20 % external)
Phenol
Others include Variable and Selling Overheads

## Slide 40
Source: TechSci Research
Operating Revenue
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 | 2035.28 | 2680.0928 | 3557.1124 | 4721.1483 | 6266.1383
Option-2 | 1628.23 | 2144.0742 | 2845.6899 | 3776.9186 | 5012.9107
Option-3 | 2035.28 | 2680.0928 | 3557.1124 | 4721.1483 | 6266.1383
Operating Cost
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 | 1516 | 1975 | 2582 | 3379 | 4424
Option-2 | 1227 | 1597 | 2086 | 2728 | 3567
Option-3 | 1582 | 2062 | 2699 | 3534 | 4629
Gross Margin
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 | 519 | 705 | 975 | 1342 | 1842
Option-2 | 402 | 547 | 759 | 1049 | 1444
Option-3 | 453 | 618 | 858 | 1187 | 1637
Note: All figures are in INR Crores
Note: All figures are in INR Crores
Note: All figures are in INR Crores
Option 1 & 3: Same operating revenue because of the production of same quantity of phenol and acetone.
Option 2 : Lower operating revenue because of 20% lesser production
Option 2 :Lower operating cost because of lower intermediates production.
Option 1 : Higher operating cost because of higher utilization of raw materials.
Option 3 : Gross margin higher due to lower fixed and variable cost as it require 20 percent external sourcing of propylene (refinery and chemical grade).
200 KTPA Phenol+120 KTPA Acetone (Propane Furnace Additional)
200 KTPA Phenol + 120 KTPA Acetone, (with available propylene and benzene)
200 KTPA Phenol + 120 KTPA Acetone, (Propylene : 80 % In-house+ 20 % external)
Plant Set-up: Operating Revenue, Operating Cost, Gross Margin
Phenol

## Slide 41
Source: TechSci Research
Chart: 
| Total CAPEX | NPV | Gross Revenue (4th Year of Operation) | OPEX (100% Capacity)
Option-1 | 1769 | 6337 | 2680 | 1975
Option-2 | 1549 | 4781 | 2144 | 1597
Option-3 | 1937 | 5235 | 2680 | 2062
All values are in INR Crores
Project Sensitivity Analysis | Project Sensitivity Analysis | 
S.No. | Project Sensitivity | Profit After Tax
 |  | Option-1
 | Profit After Tax (at optimum capacity utilization) | Nil
1 | Selling Price decreases by 11%, Raw Material Price remains same | 56% decrease
2 | Increase in Raw Material price by 16.5 % with no change in selling price | 50% decrease
3 | Increase in raw material price by 9 % with decrease in selling price by 5% | 52% decrease
4 | Increase in Cost of Production by 14.5% with no change in selling price | 54% decrease
Plant Set-up: Summary
200 KTPA Phenol+120 KTPA Acetone (Propane Furnace Additional)
200 KTPA Phenol + 120 KTPA Acetone, (with available propylene and benzene)
200 KTPA Phenol + 120 KTPA Acetone, (Propylene : 80 % In-house+ 20 % external)
Phenol

## Slide 42
Recommendations & Conclusions
Phenol

## Slide 43
Conclusions & Recommendations: Market Opportunity
Deepak Phenolics has integrated unit to produce IPA from Acetone
Deepak Phenolics and SI Group India has capacity of Cumene (captive consumption)
Demand-Supply Gap (102 KT in 2022 to 862 KT in 2040) arguments the need for new player. No explanation /New plant announcement as of now
West India+ South India will Continue to be the largest region: 83% Demand (Phenol) . 80% Demand( Acetone)
Domestic Capacity Utilization : 88%
Overall, the Phenol market is expected to be more than approximately three times from 362 Thousand MT in 2021 to 1,136 Thousand MT in 2040
Significant Exports Opportunity in Nearby Countries
India is significantly (42%) imports dependent
Phenol price is primarily dependent on the fluctuating price of Propylene, Benzene and Cumene
Phenol
Downstream integration opportunities exist to produce chemical like Bisphenol A, Isopropyl Alcohol, Ketoxime etc.
Well Established technology and production of cumene as intermediate and Acetone as by product add to volume and additional revenues in this segment.
Phenol Formaldehyde Resin : 62% Demand
A substantial business opportunity exists, but there would always be a threat of new players entering the market, specifically those companies with the advantage of additional cumene capacity for captive consumption. The early entrant will influence the entry plans of possible another entrant.
Volatility in crude oil prices in the international market may result in increased costs of benzene and propylene (raw materials for Phenol).With the surplus supply of upstream products, the company can enter Phenol-based markets such as BPA, phenol-formaldehyde resins, and others & diversify its Product Portfolio..
West India is a strategic location to be tapped. Deepak Phenolics and SI Group India Ltd. already have a location advantage in the West. Indian producers are ramping up their production, and still, there is ample scope for setting up a new greenfield unit in West or South India.
Owing to the presence of various end-user industries and the marginal extent of the market penetration in the states such as Gujarat and Maharashtra, the west region dominates the Indian Acetone Market.

## Slide 44
Features | Option 1 | Option 2 | Option 3
CapEx (INR Crore) | 1769 | 1549 | 1937
OpEx (INR Crore) | 1681 | 1360 | 1756
NPV (INR Crore) | 6337 | 4781 | 5235
IRR | 21.20% | 19.22% | 17.63%
Payback Period (Years) Simple | 2.95 | 3.28 | 3.59
Propylene | Available through DFCU and Propane Furnace Addition | Up to 80% (DBN – 8500 Hrs. Operation) | External Procurement (Up to 20 Percent)
Benzene (Raw material & Feed) | Available through DFCU | Available through DFCU | Available through DFCU
Margin %(Starting from First Year of Operation | 25.52% | 24.66% | 22.25%
Options 2 & 3 have significantly lower NPV, IRR, while CapEx is marginally higher due to the addition of a gantry storage system for handling propylene.
Option 1 is most feasible in terms of execution and realization as it won’t require refinery and chemical-grade propylene sourcing from the international and domestic market.
OPaL will have sufficient propylene after the commissioning of the propane furnace. Therefore, Option 1 will have better NPV, IRR, Payback Period and margin despite having the highest CapEx
Preference Rank:
1
2
3
200 KTPA Phenol+120 KTPA Acetone (Propane Furnace Additional)
200 KTPA Phenol + 120 KTPA Acetone, (with available propylene and benzene)
200 KTPA Phenol + 120 KTPA Acetone, (Propylene : 80 % In-house+ 20 % external)
Conclusions & Recommendations: Most Suitable Plant Set-up Option
Phenol

## Slide 45
Phenol
PVC

## Slide 46
Plant Set-up Option (PVC+Phenol)
Source: TechSci Research
Operating Revenue
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 (PVC) | 1831.363 | 3094.3312 | 4093 | 5414 | 7162
Option-1 (Phenol) | 2035.28 | 2680.0928 | 3557.1124 | 4721.1483 | 6631
Option-4 | 4461.0919 | 6743.5121 | 8858 | 11640 | 15303.3424
Option 5 | 4087 | 6133 | 8097 | 10693 | 14122
Note: All figures are in INR Crores
Operating Cost
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 (PVC) | 978 | 1481 | 1940 | 2521 | 3286
Option-1 (Phenol) | 1516 | 1975 | 2582 | 3379 | 4424
Option-4 | 2622 | 3631 | 4754 | 6207 | 8115
Option-5 | 2622 | 3631 | 4754 | 6207 | 8115
Gross Margin
Chart: 
| 2027 | 2030 | 2035 | 2040 | 2045
Option-1 (PVC) | 853 | 1614 | 2153 | 2893 | 3875
Option-1 (Phenol) | 519 | 705 | 975 | 1342 | 1962
Option-4 | 1839 | 3113 | 4104 | 5434 | 7188
Option-5 | 1464 | 2501 | 3343 | 4486 | 6007
Note: All figures are in INR Crores
Note: All figures are in INR Crores
Option 1 (PVC): 350 KTPA PVC + Captive Ethylene
Option 1 (Phenol): 200 KTPA Phenol +120 KTPA Acetone
Option 4: 200 KTPA Phenol + 120 KTPA Acetone and 350 KTPA PVC Resin Plant (Propane Furnace Addition)
Option 4: : Highest due to sum of revenues of PVC, Phenol and Acetone.
Option 4: : Highest because it includes the sum of raw materials of PVC and Phenol.
Option 4: : Highest as it includes both the margins of PVC , Phenol and Acetone.
Phenol
PVC
Option 5: 200 KTPA Phenol + 120 KTPA Acetone & 350 KTPA PVC Resin Plant (Ethane Furnace Addition)

## Slide 47
Plant Set-up Option (PVC+Phenol)
Source: TechSci Research
Chart: 
| Total CAPEX | NPV | Gross Revenue | OPEX
Option-1 (PVC) | 4159 | 12736 | 3094 | 1256
Option-1 (Phenol) | 1769 | 6337 | 2680 | 1681
Option-4 | 8694 | 23758 | 6743.5121 | 3631
Option-5 | 8592 | 17990 | 6133 | 3631
All values are in INR Crores
Project Sensitivity Analysis | Project Sensitivity Analysis | 
S.No. | Project Sensitivity | Profit After Tax
 |  | Option-4
 | Profit After Tax (at optimum capacity utilization) | Nil
1 | Selling Price decreases by 11%, Raw Material Price remains same | 20% decrease
2 | Increase in Raw Material price by 16.5 % with no change in selling price | 14% decrease
3 | Increase in raw material price by 9 % with decrease in selling price by 5% | 20% decrease
4 | Increase in Cost of Production by 14.5% with no change in selling price | 18% decrease
Option 1 (PVC): 350 KTPA PVC + Captive Ethylene
Option 1 (Phenol): 200 KTPA Phenol +120 KTPA Acetone
Option 4: 200 KTPA Phenol + 120 KTPA Acetone and 350 KTPA PVC Resin Plant (Propane Furnace Addition)
Phenol
PVC
Option 5: 200 KTPA Phenol + 120 KTPA Acetone & 350 KTPA PVC Resin Plant (Ethane Furnace Addition)

## Slide 48
Features | Option 1 (PVC) | Option 1 (Phenol) | Option 4 | Option 5
CapEx (INR Crore) | 4159 | 1769 | 8694 | 8592
OpEx (INR Crore) | 1203 | 1681 | 3253 | 3253
NPV (INR Crore) | 13376 | 6337 | 25805 | 19091
IRR | 20.03% | 21.20% | 19.20% | 15.81%
Payback Period (Years) Simple | 3.22 | 2.95 | 3.27 | 3.95
Propane (Raw material & Feed) | Propane through Parent Company ONGC | Propane through Parent Company ONGC | Propane through Parent Company ONGC | Propane through Parent Company ONGC
EDC/ VCM (Raw material & Feed) | Not Required | Not Required | Not Required | Not Required
Benzene (Raw material & Feed) | Not Required | Available through DFCU | Available through DFCU | Available through DFCU
Chlorine Sourcing | Chlor-Alkali units (DCM Sriram, Meghmani, GACL) in proximity | Not Required | Chlor-Alkali units (DCM Sriram, Meghmani, GACL) in proximity | Chlor-Alkali units (DCM Sriram, Meghmani, GACL) in proximity
Jetty Facility | Not Required | Not Required | Not Required | Not Required
Co-product Realization | NA | NA | Yes | Yes
OPaL will have sufficient ethylene, propylene and benzene after commissioning the propane furnace. Therefore, Option-4 will have better NPV, IRR, Payback Period and margin (coproduct revenue realization) despite having the highest CapEx.
Incremental ethylene and propylene availability due to other propane furnaces increase the incremental margin.
Option 1 (PVC): 350 KTPA PVC + Captive Ethylene
Option 1 (Phenol): 200 KTPA Phenol +120 KTPA Acetone
Option 4: 200 KTPA Phenol + 120 KTPA Acetone & 350 KTPA PVC Resin Plant (Propane Furnace Addition)
Recommendations: Most Suitable Plant Set-up Option (PVC+Phenol)
Phenol
PVC
PROJECT IMPLEMENTATION SCHEDULE |  |  |  |  |  |  | 
Stage | Planning | Plant Set-up |  |  |  | Operations | 
 |  | Civil Work | Plant and Machinery | Power and Water | Others | Training and Personnel | Start -up/Commercial Production
Star-End (Month) | 0-12 | 6-36 | 4-44 | 16-22 | 36-42 | 42 | 44-48
Tenure (Month) | 12 | 30 | 40 | 6 | 6 | 1 | 4
Option 5: 200 KTPA Phenol + 120 KTPA Acetone & 350 KTPA PVC Resin Plant (Ethane Furnace Addition)

## Slide 49
Recommendations: Most Suitable Plant Set-up Option (PVC+Phenol)
Phenol
PVC
Net Margin Change for Existing Co-Products |  | 
Particulars | Propane Furnace Addition | Ethane Furnace Addition
PVC and Phenol Projects both included |  | 
Net Revenue Change (INR Cr) | 5728 | 4577
If OPaL does not go for PVC |  | 
Net Revenue Change (INR Cr) | 4321 | 3170
If OPaL does not go for Phenol |  | 
Net Revenue Change (INR Cr) | 4173 | 3022
If OPaL doesn't go for both PVC & Phenol Projects |  | 
Net Revenue Change (INR Cr) | 2766 | 1614
Propane Furnace has INR 851 Crore more revenue than Base Case when additional Ethylene and Propylene are converted to Polyethylene and Polypropylene.
For 250 KTPA Polyethylene (PE) plant, the total capital investment is around 1000 INR Crore and for 120 KTPA Polypropylene (PP) plant it is not more than 500 INR Crore in case Propane Furnace is selected.
Propane is easier for procurement as feed compared to Ethane.

## Slide 50
Annexure

## Slide 51
Assumptions
1. For the calculation of total capital investment, equipment cost is derived through conducting various primary interviews with industry experts.
2. To calculate the plant's direct cost, the standard norms have been considered against the equipment cost. The below listed are the following norms-
- Purchased equipment installation: 20%
-Instrumentation and controls (installed): 18%
-Piping (installed): 2%
-Electrical (installed): 1%
-Buildings (including services): 2%
-Service facilities (installed): 5%
Note- The plant direct cost includes the equipment cost plus the above-listed parameters.
3. Total indirect plant cost includes Engineering and supervision, Construction expenses, Legal expenses, Contractor’s fee, Contingency, etc. which have been calculated using standard norms against the equipment cost.
4. ISBL facility includes equipment required in the process to manufacture PVC which constitutes around 70% of the total equipment cost. OSBL facility includes wastewater treatment plants, effluent treatment plants, different types of wet scrubbers to mitigate GHG emissions contributing about 20% to the equipment cost.
5. Total fixed capital investments is the summation of plant direct and indirect cost.
6. For calculating some of the parameters of operating cost, the following standard norms have been considered for PVC-
-Packaging Cost (calculated): 1% of Annual Sales Revenue @ 100 Percent Capacity Utilization
- Maintenance and repairs: 1.5% of Total Capital Investment
-Plant Overhead and Administrative Costs: 7.5% of Maintenance and repairs + Labour
-Distribution and selling costs: 2.5% of Annual Sales Revenue @ 100 Percent Capacity Utilization
-Research and development costs: 1.5% of Total Capital Investment
7. Expenditure of capital investment will be in the following phase-
-5% of Total Capital Investment: 2023
-25% of Total Capital Investment: 2024
-35% of Total Capital Investment: 2025
-35% of Total Capital Investment: 2026
8. Operating Revenue is bifurcated between-
- 350000 tons PVC merchant sale in option 1.
- 500000 tons PVC merchant sale in option 2.
- 500000 tons PVC merchant sale in option 3.
- 350000 tons PVC, 200000 tons Phenol, 120000 Acetone and coproducts merchant sale in option 4.
9. Operating revenue for each year is calculated by multiplying the capacity utilization for respective year to the annual sales revenue @ 100 percent capacity utilization considering inflation rate.
10. Operations will start in 2027.
11. Cash flow has been calculated till 2046.
12. Total operating cost is calculated based on capacity utilization at that period.
13. Inflation rate has been considered as 4.5%.

## Slide 52
Abbreviations

## Slide 53
CONTACT US
TechSci Research – North America
2950, Boundary Road, Burnaby, British Columbia, Canada
Tel: +1- 646- 360-1656
E: sales@techsciresearch.com
TechSci Research – Europe
54, Oldbrook, Bretton,
Peterborough,
United Kingdom
E: sales@techsciresearch.com
TechSci Research – Asia-Pacific
B-44, Sector -57, Noida, National Capital Region, UP, India
Tel: +91-120-4523900
E: sales@techsciresearch.com
TechSci Research
Cyber City, Building No. 8C, Gurgaon, National Capital Region, Haryana, India
Tel: +91-124-6428661
E: sales@techsciresearch.com
2022 © TechSci Research All Rights Reserved.
www.techsciresearch.com
INDUSTRY ASSOCIATIONS
Disclaimer :
The contents of this report are based on information generally available to the public from sources and primary interviews which are believed to be reliable. No representation is made that it is timely, accurate or complete. TechSci Research has taken due care and caution in compilation of data as this has been obtained from various sources including primary interviews which it considers reliable and firsthand. However, TechSci Research does not guarantee the accuracy, adequacy or completeness of any information and it is not responsible for any errors or omissions or for the results obtained from the use of such information and especially states that it has no financial liability whatsoever to the subscribers / users of this report. The information herein, together with all estimates and forecasts, can change without notice. All the figures provided in this document are indicative of relative market size and are strictly for client’s internal consumption. Usage of the same for purpose other than internal will require prior approval of TechSci Research.